## Slide 1: CHAPTER 1 Introduction to Computer Networks
Notes: Our goal:
get “feel” and terminology
more depth, detail later in course
approach:
  use Internet as example

## Slide 2: OUTLINE
About the course
What’s the Internet?
What’s the protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, Internet structure
Network topology
Network Performance: loss, delay, throughput
Internet Structure
OSI model & TCP/IP model

## Slide 3: 1. About the course

## Slide 4: ABOUT THE COURSE
Title: COMPUTER NETWORKS
Period: Semester I, 2020 – 2021
Google Classroom: 18Nh1x – Computer Networks
Assignments:
  Need to finish before deadline
  Submit on Classroom
  A missing assignment = -2 points in Mid-term exam
  Mid-term exam: Multiple choices or Writing
  Final exam: Multiple choices
Lecturer: PhD. Le Tran Duc
  Research Interests:
    Networking, FANET, VANET, LoRaWan, WLAN
    Network Security, Malware Analysis
    E-mail: letranduc@dut.udn.vn & Tel: 0931733853
Notes: x = 4  Class code 7gq6fu4
x = 5  Class code v3x5yvk
Introduce the Google Classroom

## Slide 5: REFERENCES
    Slides & Notes from lecturer
    Kurose, J., & Ross, K. (2017). Computer Networking: A Top-Down Approach, Global Edition.
    Nguyễn Tấn Khôi (2004). Giáo trinh môn học Mạng máy tính. Trường ĐHBK - ĐHĐN
    Tanenbaum, A., & J Wetherall, D. (2011). Computer Networks.
    Forouzan, A. B. (2012). Data communications & networking (sie). Tata McGraw-Hill Education.
    Forouzan, B. A., & Mosharraf, F. (2012). Computer networks: a top-down approach (p. 931). McGraw-Hill.
    Forouzan, B. A. (2010). TCP/IP protocol suite. McGraw-Hill, Inc..

## Slide 6: 2. What’s the Internet?

## Slide 7
Billions of connected computing devices:
  hosts = end systems
  running network apps
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Packet switches: forward packets (chunks of data)
  routers and switches
smartphone
PC
server
wireless
laptop
wired
links
wireless
links
WHAT’S THE INTERNET: “NUTS & BOLTS” VIEW?
Notes: Nuts and bolts: Những nhân tố/thành phần cơ bản
Further reading: The future of the internet – And how to stop it (Jonathan Zittrain)
In many ways, packets are analogous to trucks, communication links are analogous to highways and roads, packet switches are analogous to intersections, and end systems are analogous to buildings. Just as a truck takes a path through the transportation network, a packet takes a path through a computer network.

## Slide 8: WHAT’S THE INTERNET: “NUTS & BOLTS” VIEW?
Internet: “network of networks”
  Interconnected ISPs
Protocols control sending, receiving of messages
  e.g., TCP, IP, HTTP, Skype, 802.11
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force

## Slide 9: 3. What’s the protocol

## Slide 10: WHAT’S A PROTOCOL?
Human protocols:
  “what’s the time?”
  “I have a question”
  introductions
… specific messages sent
… specific actions taken when messages received, or other events
Network protocols:
  machines rather than humans
  all communication activity in Internet governed by protocols
protocols define format, order of messages sent and received among network entities, and actions taken on message transmission, receipt

## Slide 11: 4. Network STRUCTURE

## Slide 12: A CLOSER LOOK AT NETWORK STRUCTURE
Network edge:
  hosts: clients and servers
  servers often in data centers
Access networks, physical media:
  wired, wireless communication links
Network core:
  interconnected routers
  network of networks
End-system interaction

## Slide 13: ACCESS NETWORK
Q: How to connect end systems to edge router?
Home Access: DSL, Cable, FTTH, Dial-Up & Satellite
Access in the Enterprise (and the Home): Ethernet and WiFi
Wide-Area Wireless Access: 3G, LTE, 4G &5G
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 14: PHYSICAL MEDIA
Bit: propagates between transmitter/receiver pairs
Physical link: what lies between transmitter & receiver
Guided media:
  signals propagate in solid media: copper, fiber, coax
Unguided media:
  signals propagate freely, e.g., radio
Twisted pair (TP)
Two insulated copper wires
  Category 5: 100 Mbps, 1 Gbps Ethernet
  Category 6: 10Gbps
Notes: The wires are twisted together to reduce the electrical interference from similar pairs close by.
Typically, a number of pairs are bundled together in a cable by wrapping the pairs in a protective shield. A wire pair constitutes a single communication link.

## Slide 15: PHYSICAL MEDIA: COAX, FIBER
coaxial cable:
two concentric copper conductors
quite common in cable television systems
bidirectional
broadband:
  multiple channels on cable
fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s Gbps transmission rate)
low error rate:
  repeaters spaced far apart (~100km)
  immune to electromagnetic noise
Notes: Copper conductor: dây dẫn đồng
With this construction and special insulation and shielding, coaxial cable can achieve high data transmission rates. Specifically, a number of end systems can be connected directly to the cable, with each of the end systems receiving whatever is sent by the other end systems.

## Slide 16: PHYSICAL MEDIA: RADIO
Signal carried in electromagnetic spectrum
No physical “wire”
Can penetrate wall
Potentially carry a signal for long distances
Bidirectional
Propagation environment effects:
  reflection
  obstruction by objects
  interference
radio link types:
Terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., WiFi)
  54 Mbps or more
Wide-area (e.g., cellular)
  4G, 5G cellular
Satellite
  Kbps to 45Mbps channel (or multiple smaller channels)
  280 msec end-end delay
  geosynchronous versus low altitude

## Slide 17: 5. Network core

## Slide 18: THE NETWORK CORE
Mesh of interconnected routers
Packet-switching: hosts break application-layer messages into packets
  Forward packets from one router to the next, across links on path from source to destination
  Each packet transmitted at full link capacity
Network Core

## Slide 19: NETWORK CORE FUNCTIONS
routing: determines source-destination route taken by packets
  routing algorithms
forwarding: move packets from routers input to appropriate router output
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
destination address in arriving
packet’s header
Notes: - When a packet arrives at a router, the router examines the address and searches its forwarding table, using this destination address, to find the appropriate outbound link. The router then directs the packet to this outbound link.

## Slide 20: HOST SENDS PACKETS OF DATA
Host sending function:
Takes application message
Breaks into smaller chunks, known as packets, of length L bits
Transmits packet into access network at transmission rate R
  Link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
Packet transmission delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=
Notes: Packets are transmitted over each communication link at a rate equal to the full transmission rate of the link.

## Slide 21: PACKET-SWITCHING: STORE-AND-FORWARD TRANSMISSION
Takes L/R seconds to transmit (push out) L-bit packet into link at R bps
Store and forward: entire packet must arrive at router before it can be transmitted on next link
end-end delay = 2L/R (assuming zero propagation delay)
One-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
End-to-end delay if a path has N links (R rate/link) (or N-1 routers):

## Slide 22: PACKET-SWITCHING: QUEUEING DELAY & PACKET LOSS
Delay:
  Store-and-forward delays
  Queuing delays
  Propagation delays
Queuing and loss:
If arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up
Notes: - If an arriving packet needs to be transmitted onto a link but finds the link busy with the transmission of another packet, the arriving packet must wait in the output buffer.
Lưu ý phân biệt store-and-forward delay vs queuing delay  (1) là chờ cho đủ các bit để truyền, (2) là chờ để môi trường idle để truyền.
Animation: http://computerscience.unicam.it/marcantoni/reti/applet/QueuingAndLossInteractive/1.html

## Slide 23: CIRCUIT SWITCHING
End-end resources allocated to, reserved for “call” between source & dest:
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
  reserves a constant transmission rate (a fraction of link’s trans. capacity)
circuit segment idle if not used by call (no sharing)
commonly used in traditional telephone networks
End- to-end connection between the two hosts
- Four circuit switches are interconnected by four links
- Each of these links has four circuits
Notes: Tham khảo thêm: https://www.youtube.com/watch?v=9JqaMOK_Xaw

## Slide 24: PACKET SWITCHING versus CIRCUIT SWITCHING
Packet Switching | Circuit Switching
The message is broken down into small packets Every packet follows a different route | Entire message is passed There is a dedicated communication link
Not suitable for real-time services (because of its variable & unpredictable end-to-end delays) | - Excellent for real-time communications
- Better sharing of transmission capacity | - When no data is transmitted, capacity is unused, but still committed.
- Simpler, less costly | - More complicated
- Allocates link use on demand | - Pre-allocates use of the transmission link regardless of demand

## Slide 25: 6. Network topology

## Slide 26: NETWORK TOPOLOGY
Network topology is the arrangement of the elements (links, nodes, etc.) of a communication network.
There are two approaches to network topology: physical and logical.
Physical network topology refers to the physical connections and interconnections between nodes and the network—the wires, cables, and so forth.
Logical network topology refers to the conceptual understanding of how and why the network is arranged the way it is, and how data moves through it.
Notes: Tôpô vòng và lưới thường thích hợp với truyền dẫn đồng cấp (peer-to-peer).
Tôpô sao và cây thường thích hợp cho truyền dẫn sơ cấp- thứ cấp (server-client hoặc primary-secondary).
Tôpô bus thích hợp cho cả hai dạng: đồng cấp và sơ cấp- thứ cấp.
Tham khảo thêm: https://www.dnsstuff.com/what-is-network-topology

## Slide 27: 7. Network Performance

## Slide 28: FOUR SOURCES OF PACKET DELAY
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
dproc: nodal processing
check bit errors
examine the packet’s header
determine output link
typically < ms
dqueue: queueing delay
time waiting at output link for transmission onto the link
depends on congestion level of router (traffic is heavy or not)
the order of microseconds to milliseconds in practice

## Slide 29: FOUR SOURCES OF PACKET DELAY
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
dtrans: transmission delay:
the amount of time required to push all of the packet’s bits into the link
L: packet length (bits)
R: link bandwidth (bps) or trans. rate
dtrans = L/R
On the order of microseconds to milliseconds
dprop: propagation delay:
time required to propagate from the beginning of the link to the next destination
Depends on the physical medium
d: length of physical link
s: propagation speed (~2x108 m/sec – 3x108 m/sec)
dprop = d/s
dtrans and dprop
very different

## Slide 30: Exercise: Computing transmission & propagation delay
Consider the figure below, with three links, each with the specified transmission rate and link length.
Find the end-to-end delay (including the transmission delays and propagation delays on each of the three links, but ignoring queueing delays and processing delays) from when the left host begins transmitting the first bit of a packet to the time when the last bit of that packet is received at the server at the right. The speed of light propagation delay on each link is 3x10**8 m/sec. Note that the transmission rates are in Mbps and the link distances are in Km. Assume a packet length of 4000 bits. Give your answer in milliseconds.

## Slide 31: QUEUEING DELAY (REVISITED)
When is the queuing delay large and when is it insignificant?
Depends on:
Arriving rate at the queue
Transmission rate of the link
Nature of the arriving traffic (traffic arriving pattern)
R: transmission rate (bps) = rate at which bits are pushed out of the queue
L: packet length (bits)
a: average packet arrival rate
La: average rate at which bits arrive at the queue
average queueing delay
traffic intensity
= La/R
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving
than can be serviced, average delay infinite!
La/R < 1: nature of the arriving traffic affects the queuing delay
La/R ~ 0
La/R -> 1
Design your system so that the traffic intensity is no greater than 1.
Notes: Unlike the other three delays (namely, dproc, dtrans, and dprop), the queuing delay can vary from packet to packet.
For example, if 10 packets arrive at an empty queue at the same time, the first packet transmitted will suffer no queuing delay, while the last packet transmitted will suffer a relatively large queuing delay (while it waits for the other nine packets to be transmitted).
Chính vì vậy khi xem xét queuing delay người ta thường quan tâm các giá trị statistical: average queuing delay, variance of queuing delay….
Animation: http://www.ccs-labs.org/teaching/rn/animations/queue/

## Slide 32: PACKET LOSS
Queue (aka buffer) preceding link in buffer has finite capacity
Packet arriving to full queue dropped (aka lost)
Lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
Notes: Animation: http://www.ccs-labs.org/teaching/rn/animations/queue/

## Slide 33: THROUGHPUT
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
Notes: Rs: the rate of the link between the server and the router;
Rc: the rate of the link between the router and the client.

## Slide 34: THROUGHPUT
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec
Notes: If Rs < Rc, then the bits pumped by the server will “flow” right through the router and arrive at the client at a rate of Rs bps, giving a throughput of Rs bps. If, on the other hand, Rc < Rs, then the router will not be able to forward bits as quickly as it receives them. In this case, bits will only leave the router at rate Rc, giving an end-to-end throughput of Rc.

## Slide 35: THROUGHPUT: INTERNET SCENARIO
10 connections (fairly) share backbone bottleneck link R bits/sec
Per-connection end-end throughput: min(Rc,Rs,R/10)
In practice: Rc or Rs is often bottleneck (access network) because the core of the Internet is over-provisioned with high speed links that experience little congestion

## Slide 36: THROUGHPUT: EXERCISE
Consider the scenario shown below, with four different servers connected to four different clients over four three-hop paths. The four pairs share a common middle hop with a transmission capacity of R = 300 Mbps. The four links from the servers to the shared link have a transmission capacity of RS = 70 Mbps. Each of the four links from the shared middle link to a client has a transmission capacity of RC = 80 Mbps per second. You might want to review Figure 1.20 in the text before answering the following questions:
What is the maximum achievable end-end throughput (in Mbps) for each of four client-to-server pairs, assuming that the middle link is fair-shared (i.e., divides its transmission rate equally among the four pairs)?
Which link is the bottleneck link for each session?
Assuming that the senders are sending at the maximum rate possible, what are the link utilizations for the sender links (RS), client links (RC), and the middle link (R)?

## Slide 37: 8. Internet Structure

## Slide 38: INTERNET STRUCTURE: NETWORK OF NETWORKS
End systems connect to Internet via access ISPs (Internet Service Providers)
  residential, company and university ISPs
Access ISPs in turn must be interconnected.
  so that any two hosts can send packets to each other
Resulting network of networks is very complex
  evolution was driven by economics and national policies rather than by performance considerations.
Let’s take a stepwise approach to describe current Internet structure

## Slide 39: INTERNET STRUCTURE: NETWORK OF NETWORKS
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 40: INTERNET STRUCTURE: NETWORK OF NETWORKS
Option: connect each access ISP to every other access ISP?
access
net
access
net
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
access
net
access
net
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…

## Slide 41: INTERNET STRUCTURE: NETWORK OF NETWORKS
Option: connect each access ISP to one global transit ISP?
Customer and provider ISPs have economic agreement.
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
global ISP
Notes: Since the access ISP pays the global transit ISP, the access ISP is said to be a customer and the global transit ISP is said to be a provider

## Slide 42: INTERNET STRUCTURE: NETWORK OF NETWORKS
But if one global ISP is viable business, there will be competitors …. which must be interconnected
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
peering link
Internet exchange point
IXP

## Slide 43: INTERNET STRUCTURE: NETWORK OF NETWORKS
… and regional networks may arise to connect access nets to ISPs
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
peering link
Internet exchange point
Notes: In reality, although some ISPs do have impressive global coverage and do directly connect with many access ISPs, no ISP has presence in each and every city in the world. Instead, in any given region, there may be a regional ISP to which the access ISPs in the region connect.

## Slide 44: INTERNET STRUCTURE: NETWORK OF NETWORKS
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
peering link
Internet exchange point
Content provider network

## Slide 45: INTERNET STRUCTURE: NETWORK OF NETWORKS
Notes: IXP: Internet Exchange Point  meeting point where multiple ISPs can peer together.

## Slide 46: 9. OSI model & TCP/ip Model

## Slide 47: ORGANIZATION OF AIR TRAVEL
a series of steps  But there are functions repeated!!
Describe the airline system

## Slide 48: LAYERING OF AIRLINE FUNCTIONALITY
 The airline functionalities are divided into layers
Layers: each layer implements a service
  by performing certain actions within that layer
  relying on services provided by layer below
Look at the functionality in a horizontal manner

## Slide 49: INTERNET PROTOCOL STACK
Application: supporting network applications
  FTP, SMTP, HTTP, DNS
  The app. in one end system using the protocol to exchange message (packets of information) with the app. in another end system
Transport: process-process data transfer, flow control
  TCP, UDP
  Reliable end-to-end delivery service
  Transport application-layer messages
  Transport-layer packet = segment
Network: routing of IP packet from source to destination
  Provides the service of delivering the segment through a series of routers to the transport layer in the destination host
  IP, routing protocols
Link-layer: data transfer between neighboring network elements
  To move a frame from one node to the next node in the route
  Reliable delivery between 2 adjacent nodes
  Ethernet, 802.11 (Wi-Fi), PPP
Physical: bits “on the wire”  Move individual bits within the frame from one node to the next
application
transport
network
link
physical

## Slide 50: OSI REFERENCE MODEL
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical

## Slide 51: OSI REFERENCE MODEL

## Slide 52: ENCAPSULATION
Figure shows the physical path:
data takes down a sending end system’s protocol stack
up and down the protocol stacks of a link-layer switch and router
up the protocol stack at the receiving end system.
A packet has two types of fields: header fields and a payload field.
The payload is typically a packet from the layer above.